## Slide 1: Characterization of III-V MQW LED
EEE 460 : Optoelectronics Laboratory
Submitted to:
Dr. Muhammad Anisuzzaman Talukder
Professor, Department of EEE, BUET
Mumtahina Islam Sukanya
Lecturer, Department of EEE, BUET
Group: 01
Presented By
Mrinmoy Kundu -1706001
Elin Ranjan Das -1706004
Md. Jawad Ul Islam -1706003
Aroni Ghosh -1706004

## Slide 2: Objective
To investigate the characteristics of III-V MQW LED devices for near-infrared and visible wavelength emission.
To analyze the effect of different parameters (temperature, quantum well width, and well number of the LED) on the tunable performance of III-V MQW LED
To analyze spontaneous emission rate and optical extraction mechanism of a MQW structure using MATLAB and Lumerical software.

## Slide 3: Why III-V based MQW?
III-V materials promising for visible LED applications due to their bandgap tunability and high electron mobility.
Density of states g(E) is constant and does not depend on the electron energy, and huge value of g(E) at band edge.
Enhanced radiative recombination probability and carrier confinement in the 2DEG region

## Slide 4: Material Selection
Material | Wavelength | Typical number of layers (limited by fabrication process, found from literature)
GaAs-AlGaAs or AlAs-AlGaAs | 600-800 nm | ~55
GaN-InGaN or AlGaN-InGaN | 300-400 nm | ~12

## Slide 5: Typical III-V MQW LED Structure

## Slide 6: Spontaneous Emission Rate
Rsp(E) for a MQW LED can be expressed in
Pem . Nj(E) .fn(E2). [ 1 – fn(E1)]
Here,
Emission Transition Probability, Pem = 1/trec
Joint density function, Nj(E)
fn is the Fermi-Dirac distribution of electron

## Slide 7: Joint density function Nj(E)
Selection rules for infinite quantum well: Δn = 0
The joint density of states of 2D quantum well is -
mr =reduced electron mass, EiC and EiV are the i’th sub-bands for conduction and valence band, d= well width

## Slide 8: DOS for MQW Structure
GaAs, d= 5nm, N= 100 wells

## Slide 9: Carrier Dynamics
Rate equations governing carrier mechanisms in the QW and cladding layers are as follows
At steady state,
Nw = nw.A.d and I = J.A, final expression for τrec and nw becomes in terms of current density J

## Slide 10: Emission Spectra
Spontaneous emission spectra provide important characteristics about LED:
Emission Peak (678.6 nm)
Spectral linewidth(FWHM = 6.6 nm)
Photon flux
Internally generated optical power

## Slide 11: Peak Wavelength vs well width
With increasing well width, ground state of well gets closer to Ec and the transition energy decreases to Eg and hence the emission peak saturates to λEg eventually.

## Slide 12: P-J curve for varying QW numbers
Multiple QW emission enhancement are governed by two main mechanisms:
Multiple QWs can be thought of as independent QWs, so increasing QW number results in more electron and holes available for recombination.
Active region volume increases linearly with QW number.

## Slide 13: I-V curve
Multiple QW requires less build-in potential travelled by an electron along the depletion layer to reach the well. Thus, less potential required for photogeneration.

## Slide 14: Temperature effect on Rsp
For temperature increase, Bandgap decreases. So emission occurs at lower energies and peak emission wavelength increases.
However, for wide well, multiple peaks are observed as closely spaced higher energy levels contribute to the emission.

## Slide 15: Optical Extraction with FDTD simulation
For surface emission, effect of quantum well number and effect of geometry on external quantum efficiency of the LED is shown.

## Slide 16: Luminous efficiency
From eye sensitivity and emission spectrum, luminous efficiency can be calculated by
Luminous efficiency = 0.0532

## Slide 17: P-J Curve for complete structure
After calculating the extraction and luminous efficiency, extracted light power was reduced by a factor of
~1000.

## Slide 18: Lambertian Emission Pattern
Emission Pattern For Rectangular geometry (nQW = 4)
Emission Pattern For hemispherical geometry (nQW = 4)

## Slide 19: Comparison with Homojunction LED
Photon flux for
Homojunction LED= 4.45x1015 s-1
MQW LED= 4.32x1017 s-1

## Slide 20
Thank You!